## Slide 1
M.Tech Thesis · Experiment 2
Rotary (Furuta) Inverted Pendulum
Modelling and experimental comparison of linear and sliding-mode controllers
April 2026
Piyush Tiwari | M.Tech (Control & Automation) | IIT Kanpur

## Slide 2
Problem Framing, Contributions, and Roadmap
This deck keeps the hardware reality, the modelling choices, and the controller mathematics on the same thread.
Problem framing
• Upright-only balancing on a real stepper-driven Furuta rig
• Measured base angle, but actuation still happens through open-loop STEP/DIR
• Goal: show what it takes to make this experimentally repeatable
Project contributions
• Measured-stepper retrofit using an AS5600 on the motor axis
• First-principles L-shaped rig model with acceleration-input control design
• Three upright controllers on one hardware platform
Roadmap
• Hardware and sensing
• Model and filter design
• Linear, hybrid SMC, full-state SMC
• Pinned experimental comparison
Thesis stance
• The analytic laws are derived cleanly, but each one is followed by the firmware protections required by the stepper platform.
• Acceleration is treated as the abstract control input because that matches the actual firmware path: acceleration → commanded speed → stepper.
• The comparison is rigorous but honest: it uses seven pinned runs H1–H3, N1, and T1–T3, so conclusions are qualitative and metric-based, not statistical.
2 / 38

## Slide 3
Motivation and Problem Statement
The project is interesting because the plant is classic, but the actuator and sensing stack are not.
Why not just use a standard servo rig?
• The base is driven by a NEMA17 stepper through FastAccelStepper, not by a torque-controlled servo.
• Missed motion is possible under load, so commanded step count is not enough for feedback.
• The work is therefore both a controls problem and a hardware-software integration problem.
Practical problem statement
• Keep the pendulum upright near α = 0 while respecting ±80° base travel and ±30° pendulum safety limits.
• Estimate the required states at 200 Hz from noisy absolute encoders on a multiplexed I²C bus.
• Compare a linear controller, a pendulum-surface SMC, and a full-state surface SMC on the same rig.
Naive failure mode
If the controller asks for recovery torque that the stepper cannot realize, the measured state continues to look bad, and the controller can keep demanding more aggressive motion until the pendulum leaves the upright window.
Thesis objective
Build a technically defensible pipeline from hardware retrofit to modelling to controller implementation and quantify what each controller actually does on the real platform.
3 / 38

## Slide 4
Why Is the Furuta Pendulum Hard?
The instability is fast, the plant is underactuated, and this platform adds actuator mismatch on top of that.
Equation
Open-loop pole
$\lambda=\pm 12.47\ \mathrm{rad/s}$
Base travel
$|\theta| \le 80^\circ$
Engage window
$|\alpha|<3^\circ,\ |\dot{\alpha}|<20^\circ/s$
Classical difficulty
• Underactuated system: the pendulum is not actuated directly; only the base is.
• The unstable mode is fast enough that estimation and actuation lag matter immediately.
• Nonlinear gravity and centrifugal coupling remain active even near upright.
Platform-specific difficulty
• The controller computes acceleration, but the firmware realizes it by integrating to a speed command.
• The base is measured in closed loop, but the motor itself is still commanded open loop.
• Sensor mux glitches, missed steps, and mechanical travel limits all feed back into control design.
4 / 38

## Slide 5
Hardware Overview
This is a custom stepper-driven rotary inverted pendulum with an L-shaped pendulum and dual absolute encoders.
Figure
Custom stepper-driven Furuta rig used for all experiments.
Main hardware stack
• Arduino Mega 2560 + TMC2209 + FastAccelStepper
• NEMA17 stepper at 1600 microsteps/rev
• Two AS5600 absolute encoders via PCA9548A mux
Mechanical plant
• Horizontal arm rotating about the vertical base axis θ
• L-shaped pendulum with horizontal pivot shaft and vertical swinging segment α
• Three 688RS bearings supporting the pendulum pivot
5 / 38

## Slide 6
KEY CONTRIBUTION
Sensor Architecture: Two AS5600s Through One I²C Mux
The sensing path is simple in concept but critical in practice because both encoders share the same fixed AS5600 address.
Pendulum\nAS5600
→
Base\nAS5600
→
PCA9548A\nchannel select
→
200 µs\nsettle delay
→
Arduino\nWire @ 400 kHz
Measurement details that matter
• Channel 0 reads α, channel 1 reads θ.
• Both sensors are 12-bit absolute encoders over [0, 360°).
• The firmware averages 25 calibration samples to reduce roughly 0.5° single-sample noise.
Why this deserves emphasis
• The mux is not cosmetic; it is the enabling mechanism that makes dual-AS5600 sensing possible on one bus.
• Noise handling starts at the wiring and magnet geometry, not only in software.
• Every later derivative and controller estimate depends on this sensing path being trustworthy.
6 / 38

## Slide 7
KEY CONTRIBUTION
Stepper Motor → Measured Axis: Closed-Loop Base Tracking Retrofit
The stepper is still commanded open loop, but the output shaft is now directly measured by a coaxial AS5600 assembly.
Figure
Figure
Figure
Front view
Back view
Mounted on the motor base
Physical trick
• A magnet is fixed coaxially to the motor output shaft.
• A rigid 3D-printed housing keeps the AS5600 aligned with controlled air gap.
• This turns the motor axis into a measured state instead of trusting commanded steps.
Why it is not a true servo yet
• The controller now knows the actual base angle θ.
• But the TMC2209 still receives STEP/DIR speed commands, not torque commands.
• So the measured axis is closed-loop in sensing, while actuation remains open-loop in realization.
7 / 38

## Slide 8
Hardware Constraints and Limitations
The controller design is shaped as much by hardware limits as by the equations.
Mechanical travel
• Base hard limit: $|\theta|>80^\circ$
• Soft outward clamp begins near $78^\circ$
• Pendulum hard limit: $|\alpha|>30^\circ$
Actuation mismatch
• No torque control
• Acceleration integrated to commanded speed
• Motor can stall or miss motion
Loop timing
• $T_s=5$ ms
• 200 Hz control loop
• About 50 Hz logging
Stall monitor
• Expect motion above 500 steps/s
• Warn if $|\Delta\theta|<0.10^\circ$ for 150 ms
What this means for controller design
• The implemented law must be stepper-friendly: bounded speed, bounded acceleration, and robust to missed motion.
• Any claim of stability must be read together with the firmware aborts, soft limits, and actuator shaping.
Firmware response to failure
• Soft-limit suppression near the base stop
• Predictable disarm to IDLE after debounced limit violation
• Auto-rearm only after the pendulum re-enters the engage window
8 / 38

## Slide 9
State Machine: Calibrate → Idle → Active
The control software is organized around an explicit state machine instead of a monolithic loop with hidden assumptions.
CALIBRATE
→
IDLE
→
ACTIVE
Engage logic
• Require $|\alpha|<3^\circ$ and $|\dot{\alpha}|<20^\circ/s$
• Hold the condition for 20 ticks = 100 ms before engage
• Keep derivative history warm when transitioning from IDLE to ACTIVE
Disarm logic
• Debounced FALLEN detection over 3 ticks
• Immediate nonlinear abort outside the upright-only SMC window
• Disable stepper outputs and return to IDLE in a predictable way
9 / 38

## Slide 10
Measurement Pipeline Before Any Controller Sees the States
The estimator is intentionally simple, but the preprocessing around it is where most of the practical robustness comes from.
Read raw\nα, θ
→
Wrap-safe\nangle diff
→
Reject >30°\none-tick jumps
→
Tustin\nderivative filter
→
Clamp\nα̇, θ̇
Key numerical settings
• Nominal loop: 200 Hz, logging: about 50 Hz
• Jump rejection threshold: $30^\circ$ per control tick
• Derivative clamps: $|\dot{\alpha}|, |\dot{\theta}| \le 300^\circ/s$
Why this stage is central
• Both SMC surfaces depend directly on α̇, so bad derivative estimates immediately corrupt the control law.
• The glitch handling forces impossible jumps to zero before the filter sees them.
• This is why the estimator deserves a dedicated section rather than a one-line implementation note.
10 / 38

## Slide 11
Modelling Strategy and Assumptions
The model is idealized for control design, but the rig-specific geometry is retained instead of collapsing to the usual simplified pendulum picture.
Assumptions
• Rigid links and frictionless joints
• No missed steps, no sensor glitches, no actuator saturation inside the analytic model
• Commanded base acceleration θ̈ treated as the abstract input
Geometry retained
• L-shaped pendulum instead of a single uniform rod
• Mass split between non-swinging shaft mass and swinging mass
• Pendulum COM computed from the real vertical rod plus tip mass
Grouped constants
• $K = m_p L_r l_p$
• $G = m_p g l_p$
• $\hat J_0 = \hat J_1 + m_p L_r^2$
Design choice to remember
Torque appears in the full Euler–Lagrange equations, but the controller chapters intentionally rewrite the upright dynamics in acceleration-input form because that is the quantity the firmware can shape most directly.
11 / 38

## Slide 12
Kinematics and Coordinates
The coupling between arm rotation and pendulum swing appears already at the position and velocity level.
Coordinates
• $\theta$: base yaw angle
• $\alpha$: pendulum angle, with $\alpha=0$ upright
• $L_r$: motor axis to pendulum pivot
• $l_p$: pivot to pendulum COM
Equation
Interpretation
The mixed term $2L_r l_p \cos\alpha\,\dot{\theta}\dot{\alpha}$ is the first clear sign that arm motion and pendulum motion are dynamically coupled even before the equations of motion are formed.
12 / 38

## Slide 13
Energies, Lagrangian, and Nonlinear Equations of Motion
Once the rig-specific kinetic energy terms are retained, the Euler–Lagrange equations expose the exact nonlinear structure later used by the SMC designs.
Equation
Equation
What matters later
These equations preserve the $\hat J_2\sin^2\alpha$ inertia modulation, the $\sin\alpha\cos\alpha\,\dot\theta^2$ centrifugal effect, and the coupling through $K\cos\alpha$, which are precisely the terms the nonlinear controllers exploit.
13 / 38

## Slide 14
KEY CONTRIBUTION
What Our Model Retains vs Common Simplified Furuta Models
The point is not rhetorical superiority; it is that several small-looking terms are exactly the ones that matter when you move from a teaching model to a custom stepper rig.
Feature
Common simplified model
This thesis model
Pendulum geometry
Uniform rod abstraction
Actual L-shaped geometry with shaft mass separated from swinging mass
Yaw inertia term
Often constant
Retains $\hat J_2\sin^2\alpha$ inside the mass matrix
Pendulum rotational KE
Often collapsed or omitted
Retains $T_{\mathrm{rot}}=\tfrac12J_p(\dot\alpha^2+\sin^2\alpha\,\dot\theta^2)$
Centrifugal coupling
Often dropped near upright
Retains $\sin\alpha\cos\alpha\,\dot\theta^2$ explicitly
Control input used later
Motor torque
Commanded base acceleration matched to firmware architecture
Takeaway
The retained terms are not decorative complexity; they are the nonlinear structure that later appears again in the hybrid and full-state SMC derivations.
14 / 38

## Slide 15
KEY CONTRIBUTION
Acceleration as Input: Why and How
The decisive modelling move is to redesign the plant around the quantity the firmware can shape: commanded base acceleration.
Equation
Controller\ncomputes θ̈
→
Integrate to\ncommanded θ̇
→
FastAccelStepper\nspeed command
Why this is architecturally cleaner
• The control law becomes independent of the driver current-control internals.
• The model matches the actual firmware path instead of pretending the stepper is torque controlled.
• The downside is explicit: the hardware does not realize the commanded acceleration perfectly under load.
Numerical constants used later
• $A = 100.8$
• $B = 1.952$
• $k_s = 4.444\ \mathrm{step/deg}$
15 / 38

## Slide 16
Linearisation About Upright
Around α ≈ 0 the dynamics simplify enough for transparent state-space design while still keeping the main unstable physics visible.
Equation
Open-loop fall rate
$\lambda = \pm \sqrt{G/J_{eq}} = \pm 12.47\ \mathrm{rad/s}$
Why this linearisation is still useful
• It exposes the unstable pendulum mode and the base-to-pendulum control effectiveness directly.
• It gives a compact four-state plant for pole placement and LQR.
• It is also the benchmark against which the nonlinear controllers are judged.
What it does not capture
• Nonlinear gravity $A\sin\alpha$ away from small angles
• Centrifugal coupling $\sin\alpha\cos\alpha\,\dot\theta^2$
• Actuator saturation, missed steps, and sensing glitches
16 / 38

## Slide 17
State-Space Representation
The linear controller sees the rig as a four-state acceleration-input plant.
Equation
Interpretation
• θ̈ acts directly on θ̇
• The same θ̈ also drives α̈ through −B
• α feeds back as the unstable mode through A
Why this form is convenient
It gives a direct bridge from the modelling chapter to controller synthesis: one can place poles analytically, derive an LQR gain, and then convert the result into stepper acceleration units using the fixed conversion $k_s=4.444$.
17 / 38

## Slide 18
Real Firmware Control Architecture
This is the practical control-system block diagram actually implemented in the firmware, not an idealized textbook loop.
AS5600\nθ, α
→
Mux select\n+ settle
→
Wrap +\nglitch reject
→
Tustin\nfilter
→
Controller
→
Sign map
→
θ̈ → θ̇\nintegrator
→
Deadband +\nreverse stop + limits
→
FastAccelStepper\n→ motor
Where the architecture differs from a servo textbook
• The controller closes the loop around measured θ and α, but the actuator channel is still speed-command based.
• The accel-to-speed integrator and speed deadband are part of the plant as seen by software.
• This is why practical protections are not optional add-ons.
Explicit protection layers
• Soft-limit suppression near ±80°
• Stop-before-reverse to avoid direction chatter
• Stall diagnostics based on measured θ, not only commanded speed
18 / 38

## Slide 19
KEY CONTRIBUTION
State Estimation: Bilinear Derivative Filter
The derivative filter is mathematically small, but it is one of the highest leverage implementation choices in the whole project.
Equation
Implemented coefficients
$b_0 = \frac{2\omega_c}{2+\omega_c T_s},\qquad a_1 = \frac{\omega_c T_s - 2}{\omega_c T_s + 2}$
Practical estimator details
• Pendulum angle increments are wrapped into ±180° before filtering.
• Rejected jumps force the corresponding increment to zero, so the filter does not see a false spike.
• The filtered derivatives are then clamped before entering control.
Chosen operating point
• $\omega_c = 450\ \mathrm{rad/s}$, so $f_c \approx 71.6$ Hz
• $T_s = 5$ ms at 200 Hz
• Numerically: $b_0 = 211.7647,\ a_1 = 0.0588$
19 / 38

## Slide 20
Filter Coefficient Derivation and Cutoff Selection
The cutoff is high enough to keep derivative lag small, but the roll-off is still strong enough to tame encoder quantization and mux glitches.
Equation
Why not recompute every tick?
The firmware measures actual dt for integrators and reference updates, but the derivative coefficients are fixed from the nominal 5 ms period to keep the implementation simple and stable.
Cutoff tradeoff
• Lower ωc: cleaner derivative, but more phase lag
• Higher ωc: sharper derivative, but more noise amplification
• Chosen value 450 rad/s was found to be a workable compromise on this hardware
Firmware-side safety around the filter
• 30° per-tick jump rejection before filtering
• Derivative clamping after filtering
• Diagnostic counters for glitch rejections and I²C faults
20 / 38

## Slide 21
Linear Full-State Feedback by Pole Placement
The baseline controller is derived analytically from the linearized acceleration-input plant.
Equation
Coefficient relations
$a_3 = k_{\dot\theta} - B k_{\dot\alpha},\ a_2 = k_\theta - A - Bk_\alpha,\ a_1 = -A k_{\dot\theta},\ a_0 = -A k_\theta$
Design idea
• Choose a fast second-order factor for the pendulum mode.
• Choose a slower second-order factor for the base-centering mode.
• Match coefficients directly instead of using Ackermann’s formula or a numerical black box.
Why this baseline matters
• The linear controller is the calmest and most interpretable controller in the thesis.
• It also provides the shared base-centering gains reused later by the hybrid and full-state SMC implementations.
21 / 38

## Slide 22
Closed-Form Gain Calculation and Stepper Conversion
The gains are first derived in degree-space dynamics and then converted into stepper acceleration units.
Equation
Firmware gains used in experiments
$K_\theta=31.5,\ K_\alpha=725.6,\ K_{\dot\theta}=28.3,\ K_{\dot\alpha}=73.5$
Unit conversion
• $k_s = 1600/360 = 4.444\ \mathrm{step/deg}$
• Theoretical gains are multiplied by ks to obtain stepper acceleration units.
• The deployed gains are then tuned on hardware while preserving the analytic structure.
Why this slide matters
• It shows the bridge from derivation to firmware constants explicitly.
• The gains shown in code are not arbitrary empirical numbers; they sit on top of a closed-form design path.
22 / 38

## Slide 23
LQR as a Secondary Design Path
LQR is included as a compact alternative derivation, but the thesis keeps pole placement as the main transparent design route.
Equation
Why it is not the main story
• The resulting gain depends on chosen Q/R weights rather than explicit modal targets.
• Pole placement was better for explaining the intended pendulum/base mode separation.
Why still include it
• It confirms the same linearized plant can be handled with standard optimal control machinery.
• It is useful as a cross-check and as a future tuning path if the cost function is made actuator-aware.
Design takeaway
This thesis uses LQR as supporting evidence that the linearized model is internally consistent, not as a competing headline controller branch.
23 / 38

## Slide 24
Trapezoidal Reference Profiler and Stability Gates
The nudge mode is not a separate controller; it is a reference-generation layer wrapped around the same balancing stack.
User target\nθ_target
→
Trapezoidal\nprofile
→
Stability\ngate
→
Pause /\nresume
→
θ_ref, θ̇_ref, θ̈_ref
Profile settings used in the thesis
• Target limit: $|\theta_{\mathrm{target}}| \le 35^\circ$
• Max reference speed: $12^\circ/s$
• Max reference acceleration: $60^\circ/s^2$
Pause / resume logic
• Keep moving only if $|\alpha|<5^\circ$ and $|\dot{\alpha}|<80^\circ/s$ after a 200 ms grace period
• Debounce both stable and unstable conditions for 10 ticks
• On instability, hand θref once to the current measured θ and hold there until the rig is calm again
24 / 38

## Slide 25
Implementation Tricks in Firmware
This slide collects the small choices that stop the real hardware from behaving like the ideal equations would suggest.
Wrap + glitch handling
• Wrap-safe angle differences
• Reject >30° one-tick jumps
• Keep false spikes out of α̇ and θ̇
Bias killers
• Velocity leak in linear mode only
• Auto-trim the α reference slowly
• Clamp trim to ±1.5°
Motor command shaping
• 100 ms engage ramp
• Low-speed stop deadband
• Stop-before-reverse
Watchdogs
• Base stall detection from measured θ
• Limit debounce before FALLEN
• SMC upright-only abort window
Tuning helpers
• Sign wizard for motor / θ / α / control direction
• EEPROM persistence for settings
• Runtime controller parameter commands
Why these matter
These are the difference between a controller law that looks correct on paper and a balancing session that survives repeated real-world trials.
25 / 38

## Slide 26
Linear Controller Performance
The linear controller is the cleanest performer on this rig: calm in hold mode and capable of commanded base motion without a fall.
Figure
Figure
Hold run H1
Nudge run N1
Readout
In the pinned dataset the linear controller gives the lowest hold-mode α RMS (0.513°), survives the tap run T1, and demonstrates commanded base-position moves while keeping the pendulum upright during N1.
26 / 38

## Slide 27
KEY CONTRIBUTION
Hybrid SMC: Motivation and Sliding Surface
The first nonlinear design keeps the sliding surface pendulum-centric and treats base centering as a second objective.
Equation
Interpretation
On the surface $s=0$, the pendulum follows $\dot{\alpha}=-\lambda\alpha$, so $\alpha(t)=\alpha_0 e^{-\lambda t}$ and $\lambda$ directly sets the desired decay rate.
Why move to nonlinear control
• The linear controller ignores the exact $A\sin\alpha$ gravity term and the centrifugal coupling.
• The SMC law uses the reduced nonlinear upright model directly.
• This is especially attractive for moderate excursions where the small-angle approximation is visibly coarse.
Hybrid idea
• The sliding surface handles pendulum stabilization only.
• A separate gated PD-like base-centering term is later blended in.
• This separation keeps tuning intuitive on the real rig.
27 / 38

## Slide 28
Hybrid SMC: Control Law Derivation
Start from the nonlinear acceleration-input plant, differentiate the sliding surface, and solve for the base acceleration that enforces the reaching law.
Equation
Experimental parameters
$\lambda = 15,\ K = 800,\ \phi = 50,\ \gamma = 1.0$
Numerical implementation notes
• Angles are measured in degrees, but the nonlinear trigonometric terms are evaluated in radians.
• A cosine floor protects the denominator: cos_safe = sign(cos α) max(|cos α|, 0.2).
• The resulting θ̈ command is converted into stepper acceleration units and saturated.
Why the law is attractive
• Explicit compensation of gravity and centrifugal drift
• Direct design knobs: λ for decay, K for reaching, ϕ for boundary layer width
• Still simple enough to run comfortably at 200 Hz on the Arduino Mega
28 / 38

## Slide 29
Lyapunov Stability Proof for the Hybrid SMC Reaching Law
The analytic law gives a clean reaching proof, but the firmware protections must be stated alongside it.
Equation
Finite-time reaching outside the boundary layer
The standard ideal reaching result is recovered: the surface is reached in finite time with a rate set by $K$ when $|s|>\phi$.
Theory vs firmware
• The proof applies to the analytic law before saturation, deadband, engage ramp, and abort logic are added.
• The deployed firmware also enforces the upright-only validity window, cosine protection, and acceleration limits.
• So the Lyapunov result is a design guide, not an unconditional hardware theorem.
Why keep the proof in the deck
• It explains the logic of the controller rather than presenting SMC as a tuning heuristic.
• It also shows exactly where the practical implementation begins to diverge from the ideal law.
29 / 38

## Slide 30
Boundary Layer and Chattering Elimination
The saturation function keeps the reaching law usable on the real stepper platform by softening the switching near the surface.
Equation
Chosen boundary layer
$\phi = 50\ \mathrm{deg/s}$ in the pinned dataset
Outside the layer
• The reaching term behaves like sign(s), so the controller pulls aggressively toward the surface.
• This is the part that provides the classical finite-time reaching behavior.
Inside the layer
• The law becomes locally linear and smooths the control action.
• This reduces chatter in commanded acceleration and therefore reduces harsh stepper commands near upright.
30 / 38

## Slide 31
Hybrid SMC: Base-Centering Blend
The controller is called hybrid because the pendulum-surface SMC is blended with a separate gated base-centering term.
Equation
Gate used in firmware
Enable only after 200 ms and only if $|\alpha|<5^\circ$ and $|\dot{\alpha}|<150^\circ/s$
Why the blend is needed
• A pendulum-only surface does not directly regulate the base position.
• Small biases can make the arm random-walk even while the pendulum stays near upright.
• The extra centering term is therefore a pragmatic fix for drift on the real rig.
What is special here
The two control objectives are intentionally decoupled: the SMC law dominates pendulum recovery, while the base-centering action is only allowed to act when the pendulum is already calm enough that the two objectives will not fight each other.
31 / 38

## Slide 32
Hybrid SMC Performance
The hybrid SMC suppresses peak excursions well in the pinned hold run, but the tap run shows the practical limit of aggressive recovery on this stepper platform.
Figure
Figure
Hold run H2
Tap run T2
Readout
In the pinned hold run the hybrid SMC gives the smallest max |α| and max |θ|. In the pinned tap run it eventually falls, which is consistent with the platform-level limitation that the controller can demand recovery harder than the open-loop stepper can realize.
32 / 38

## Slide 33
KEY CONTRIBUTION
Full-State SMC: Unified Sliding Surface
The third controller encodes pendulum and base objectives in one scalar sliding manifold instead of separating them.
Equation
Pinned parameters
$\lambda_{\alpha}=15,\ \lambda_{\theta}=2,\ k=0.5,\ K=800,\ \phi=50$
Interpretation of the new terms
• $\lambda_{\alpha}$ shapes pendulum decay on the surface
• $\lambda_{\theta}$ shapes base error decay
• $k$ couples base tracking into the sliding condition
What is special here
• Pendulum stabilization and base tracking are no longer separate objectives blended later.
• The denominator of the control law now depends directly on k, which makes safety analysis much more important.
33 / 38

## Slide 34
KEY CONTRIBUTION
Denominator Safety and Singularity Management in Full-State SMC
This controller is mathematically elegant, but it introduces a denominator that can become dangerously small if the coupling is not managed.
Equation
Equation
Implemented safeguards
• Cosine floor: $|\cos\alpha| \ge 0.2$ with sign preserved
• Coupling limit: $k \le 1.20$
• Coupling ramp-in over 200 ms after engage
Theory vs firmware
• The analytic law assumes denominator regularity.
• The firmware explicitly enforces that regularity by modifying k_eff and the denominator margin online.
• This is one of the clearest places where implementation-aware control design matters.
34 / 38

## Slide 35
Full-State SMC: Control Law and Implementation Safeguards
The full law is nonlinear, coupled, and explicitly actuator-shaped for the stepper platform.
Equation
SMC4-specific caps
$u_{\max}=12000\ \mathrm{steps/s^2},\ \dot{\theta}_{\max}=2000\ \mathrm{steps/s}$
Additional clamps in firmware
• Clamp $|\theta_{\mathrm{err}}| \le 78^\circ$
• Clamp $|\dot{\theta}_{\mathrm{err}}| \le 200^\circ/s$
• Clamp internal $|\dot{\alpha}| \le 200^\circ/s$ in the SMC4 math
Practical reading of this controller
• It is the most unified controller mathematically.
• It is also the most sensitive to actuator limits and denominator conditioning on this platform.
• That is why the implementation includes more shaping and more guards than the hybrid SMC.
35 / 38

## Slide 36
Full-State SMC Performance
The full-state surface controller balances upright in calm conditions, but the required protection logic is visible in both its diagnostics and its effort levels.
Figure
Figure
Figure
Hold run H3
Protected denominator
Effective coupling
Readout
In the pinned hold run the controller stays upright, but it uses much higher effort than the linear and hybrid controllers. In the pinned tap run T3 it falls, reinforcing that this controller is the most sensitive to actuator limits and safety shaping on the present hardware.
36 / 38

## Slide 37
Three-Controller Comparison
This comparison is rigorous in sourcing but intentionally modest in claim strength: it is based on one pinned run per condition.
Controller
Hold α RMS
Hold acc RMS
Tap outcome
Tap acc RMS
Linear
0.513°
1354.846
Success (T1)
1695.658
Hybrid SMC
0.826°
1465.582
Fallen (T2)
1493.067
Full-state SMC
1.61°
3364.957
Fallen (T3)
3843.042
Figure
Figure
Pinned hold metrics
Pinned tap metrics
Dataset caveat
Provenance: H1–H3, N1, and T1–T3 only. The deck therefore reports a qualitative, metric-based comparison rather than a statistical controller ranking.
37 / 38

## Slide 38
Contributions, Limitations, and Next Steps
The final message is that the thesis contributes both a model/controller stack and a practical recipe for making a custom stepper Furuta rig experimentally usable.
Main contributions
• Measured-stepper retrofit with dual AS5600 sensing
• L-shaped first-principles model with acceleration-input control framing
• Three controller implementations on one platform
Key limitations
• One pinned run per condition only
• No explicit tap onset markers
• Actuator realization still limited by open-loop stepper behavior
Next steps
• Run repeated trials per controller
• Make disturbance timing measurable
• Explore more actuator-aware nonlinear control
Most importantly, the thesis shows how much practical control rigor lives between the equations and the motor driver.
38 / 38